SKYE INSTRUMENTS LIMITED

21 Ddole Enterprise Park, Llandrindod Wells, Powys, LD1 6DF UK

Tel: +44 (0) 1597 824811   Fax: +44 (0) 1597 824812

Email: skyemail@skyeinstruments.com     Web:  http://www.skyeinstruments.com

DATAHOG2

Using with Thermocouple Sensors

The Skye DataHog2 logger has differential voltage inputs with  resolutions down to 0.1 V which are suitable for recording thermocouple measurements.

A thermistor sensor is fitted inside the datalogger housing and recorded simultaneously to provide the cold junction reference.

The DataHog2’s programming includes look up tables for 10 kohm thermistors, but does not include the same for thermocouple probes. So the output from the thermocouples are recorded in mV only and need to be converted to Degrees C in Excel or similar. This is an easy procedure and Skye provide the technical details and equations for doing this.

When setting up the DataHog2 it is advisable to choose Termination Code 00. If Codes 01 or 02 are chosen this activates a 100 kohm resistor ground reference which can give rise to errors in the measurement.