SKYE INSTRUMENTS LIMITED

21 Ddole Enterprise Park, Llandrindod Wells, Powys, LD1 6DF UK

Tel: +44 (0) 1597 824811   Fax: +44 (0) 1597 824812

Email: skyemail@skyeinstruments.com     Web:  http://www.skyeinstruments.com

## SpectroSense2 Meter – Add a Sensor

## Menu Option 8  – Edit Sensor Data

In order to view accurate, calibrated measurements from light sensors, the

SpectroSense2 meter must be configured with the sensor’s calibration data. This

meter can store a Sensor Library of data for up to 16 sensors in total, for easy

interchange between Active Sensors.

You will need to refer to the new sensor’s Calibration Certificate to enter its calibration data, and the SpectroSense2’ Configuration Certificate to allocate the sensor to the correct socket.

Menu Option 8 leads the user through a step by step process of entering the Sensor Library Number (00 to 15), Sensor Description, Sensor Output, Units and Offset.

Use the NEXT and Up / Down keys on the meter’s keypad to move the cursor, scroll through numbers 0 to 9 plus decimal place, and upper and lower case letters.